## Slide 1
“Art is never finished, only abandoned.” Leonardo da Vinci.
This piece of art can be improved in the following ways:
Use the equations describing the behaviour of the Ring to design light patterns providing quantitative descriptions of the illuminance received by the user.
Integrate the NPSC in the IoT device family
SYSTEM OVERVIEW
BACKGROUND
OBJECTIVES
Sensors
  Outside temperature
  Light temperature
WHAT’S NEXT?
Othniel KONAN
Electrical & Computer Engineering
Kylekojey@gmail.com +27783420721
NeoPixel Sunrise Clock (NPSC)
An Intelligent Bedside Clock
Studies made on human behavioural patterns have revealed that light of wavelength can affect the sleep-wake cycle by controlling the production of melatonin.
Create a device capable of generating light emission patterns which can produce both soporific and gentle awakening effects on humans, to control the human sleep-wake cycle in a more gentle manner that can have health benefits.
Two user inputs type
  Smartphone application
  Onboard touchscreen
Alarm functionality
  64KB EEPROM
  Real Time Clock
  Alarms from
Visual outputs
  Ring for emitting light of wavelength at
  Time & Weekday
  Date & Temperature
System Hierarchy
  Software
    Application (top)
    Framework (middle)
  Hardware (bottom)
RING SPECIFICATIONS
  180 neopixels
  5V @ 7.5A max
  37.5 W max
  0.5W min
  21 x 21 cm2
  RGB colours
  255 x 255 x 255 x 180 colour combinations
  Refresh rate >= 5.4ms
MATHEMATICAL MODELS
  Illuminance distribution as a function of
    the distance (cm): f(x) =
    the brightness (%): f(x) =
  Temperature (C) vs Current (A):
    f(x) =
ILLUMANCE AND BLUE LIGHT
  Blue light of 465nm wavelength capable of significantly reduce the production of the sleeping hormone emit up to 30lx at an object place 1m meter away and at 90 degree angle from the normal to the Ring’s surface.
  Illuminance distribution of the Ring follows Lambert’s Cosine Law. As expected, object positioned on the normal to the Ring’s surface receive most of the illuminance emitted.